Telecommunications Central Office Presentation Outline

University of Phoenix

Dr. Thomas T. Cobianchi

Slide 1 – Cover Page

Telecommunications Central Office

Slide 2 – Phone and Internet (Data)

Phone – analog or digital (channel – 64kps)

Internet – digital (clear channel – 128kps up to 1024kps)

Slide 3 – Fiber Optic Cable

Fiber optics – photons (glass)

Digital signal (binary – 1 or 0)

Slide 4 – Multiplex (MUX)

Distribution of signals into voice channels

24 separate 64kps channels per T1 (1.544mps - bandwidth)

Slide 5 – MUX Aisle

Equipment aisle

MUX hardware line up

Slide 6 – Digital Access Cross Connect System (DACS)

Converts fiber optic signal to electrical

Fiber Optics – photons

Copper twisted pair – electrons

STS-1 (photons) to OC1/DS1 (electrical)

OC1/DSI minimum fiber optic level

OC1/DS1 – 24 voice channels (64kps) or 1 Internet (data) channel –T1

Slide 7 – VersiPak

Distributes voice signals (dial tone)

Distributes data signals

Dynamic distribution of T1 bandwidth between voice and data

Slide 8 - 5ESS Voice Switch

Lucient/Avaya hardware

Distributes voice calls over 64kps channels

Recognizes dial tone when phone is off hook

Recognizes MOUs

Slide 9 – Internet (Data)

Transmits binary code (1 or 0)

Distributes data

Slide 10 – Uninterruptible power Supply (UPS)

AC transfer switch from external from external power source

DC transfer to battery back up source

Slide 11 – Pad Mounted Transformer

Receives power from power company distribution switchgear

Steps down voltage from 4160 volts to 230/115 volts

Transformer owned by Power Company

Slide 12 – 1 Megawatt Generator

Kicks in if there is an external power outage

Powered by diesel fuel engine

Slide 13 – Converter (AC/DC)

Converts outside power from AC to DC

Regenerates DC battery source

Slide 14 – DC Battery Back Up Power

Kicks in there is a loss of DC power

8 hour source of DC power

Recharges by AC/DC converter upon recovery of AC power

Slide 15 – A/C Condenser Fan

Outside equipment hat compresses Freon liquid into gas

Connects with inside equipment evaporative cooler – provides cooling

Component of A/C climate control equipment

Slide 16 – Monitor and Provisioning

Monitors all signals in the central office facility

Directs signal to individual customer telecommunication applications

Slide 17 – Customer Collocation Cabinet

Customer components – Internet/mail servers

Secure routers (web hosting)

Within 24/7 monitored and climate controlled facility

# Text boxes

University Of

Phoenix

University Of

Phoenix

University Of

# Phoenix